## Slide 1: Advanced Network Design EETS8332
Spring 2013
Session 1
© Dr. Scott Kingsley

## Slide 2: Dr. Scott Kingsley Bio
Employment
  U.S. Navy
  DSC Communications
  MCI Telecommunications
  Alcatel Networking Systems
Education
  BS Electronics
  MS Telecommunications
  Doctor of Engineering
Entrepreneur
  TelOptica, Inc.
  OptionTel, LLC
© Dr. Scott Kingsley
Teaching
  DeVry/Keller
  Frequent guest lecture at Texas A&M telecom
  Various others
Organizations
  IEEE
  ITERA
  ASEE

## Slide 3: Past
IP
ATM/FR
T-1/T-3/SONET

## Slide 4: North American Digital Hierarchy
© Dr. Scott Kingsley

## Slide 5: Digital Transport: Channelized T-1
© Dr. Scott Kingsley

## Slide 6: T-3
28 x T-1
Proprietary
© Dr. Scott Kingsley

## Slide 7: NADH Problems
Clocking variation
“Black box”
  Back-to-back multiplexers
Speed limitations
© Dr. Scott Kingsley

## Slide 8: SONET/SDH
SONET/SDH as part of the first generation of optical networks was the earliest to be deployed in backbone networks and has been very successful over the years.
It is particularly adept at supporting constant bit rate (CBR) connections, and it multiplexes these connections into higher speed optical connections by using time division multiplexing.
Originally designed for low speed voice and CBR connections, up to 51 Mb/s, it now supports data network, packet traffic that can have link transmission rates in the tens of gigabits per second.
An important feature of SONET/SDH is that it provides carrier grade service of high availability.
© Dr. Scott Kingsley

## Slide 9: Plesiochronous Networks
Plesio means near
Equipment has very accurate but not synchronized clocks
North American Digital Hierarchy
CSU/DSU provides clock
Disadvantages
  Speed limited
  Payload invisible
© Dr. Scott Kingsley

## Slide 10: SONET Synchronization
In SONET, all clocks in the network are locked to a master clock.

## Slide 11: SONET Advantages
Multiplexing simplicity and transparency
Management capabilities
Interoperability (standardization)
Network availability
© Dr. Scott Kingsley

## Slide 12: SONET Advantages
Multiplexing simplicity and transparency
Management capabilities
Interoperability (standardization)
Network availability
© Dr. Scott Kingsley

## Slide 13: SONET Specifications
Defines electrical & optical signal interfaces
  Electrical
    Multiplexing, regeneration performed in electrical domain
    STS – Synchronous Transport Signals defined
    Very short range (e.g., within a switch)
  Optical
    Transmission carried out in optical domain
    Optical transmitter & receiver
    OC – Optical Carrier

## Slide 14: SONET/SDH Hierarchy

## Slide 15: SONET STS-1 frame
Each STS-1 frame is 90 columns * 9 rows of bytes = 810 bytes
There are 8000 STS-1 frames per second
  so each byte represents 64 kbps (each column is 576 kbps)
Thus the basic STS-1 rate is 51.840 Mbps
90 columns
9 rows

## Slide 16: SONET Pointers

## Slide 17: SONET STS-1 Frame

## Slide 18: SONET Virtual Tributaries (VTs)
SONET is designed to carry broadband payloads. Current digital hierarchy data rates, however, are lower than ST-1. To make SONET backward-compatible with the current hierarchy, its frame design includes a system of virtual tributaries (VTs). A virtual tributary is a partial payload that can be inserted into an STS-1.

## Slide 19: SONET Virtual Tributaries (VTs)

## Slide 20: SONET Virtual Tributaries (VTs)

## Slide 21: SONET Virtual Tributaries
VT size | Rate | Payload
VT 1.5 | 1.728 Mbps | DS1 (1.544 Mbps)
VT 2 | 2.304 Mbps | E1 (2.048 Mbps)
VT 3 | 3.456 Mbps | DS1C (3.152 Mbps)
VT 6 | 6.912 Mbps | DS2 (6.312 bps)
Standard PDH rates map efficiently into SONET

## Slide 22: SONET Virtual Tributaries

## Slide 23: SONET Equipment
Terminal Multiplexer (TM)
Add-Drop Multiplexers (ADM)
Digital Cross-connect System (DCS)
Regenerator and Amplifiers

## Slide 24: SONET Equipment Review

## Slide 25: SONET Layers

## Slide 26: SONET Layers
Physical
Section
Physical
Section
Physical
Section
Physical
Section
Line
Physical
Section
Line
Physical
Section
Line
Path
Physical
Section
Line
Path

## Slide 27: SONET and OSI Layers

## Slide 28: SONET STS-1 frame
Each STS-1 frame is 90 columns * 9 rows of bytes = 810 bytes
There are 8000 STS-1 frames per second
  so each byte represents 64 kbps (each column is 576 kbps)
Thus the basic STS-1 rate is 51.840 Mbps
90 columns
9 rows

## Slide 29: SONET STS-1 Frame

## Slide 30: SONET STS-1 Frame

## Slide 31: END SESSION 1